Password Sauna Lock

Public Mode Configuration: Main Password*1, Temporary Password*1, Main Card*1, Temporary Card*1

Password: 4~15 digits.

1, Factory Reset

Press button on back side of mortise by a thin stick for 5 times, after this step, the lock status will be:

Password: 12345678

Default Mode: Home Using, Single Open

2, Change to Public Lock Mode

Main Password + Key + 7 + Key : Change to public lock mode, lock will be normal open;

3, Operations:

A, Manage Users(Operate in Normal Open and Normal Close)

1, Add Main Card: the first card reading by lock will be the main card.

2, Revise Main Password

Previous Main Password + Key + 1 + New Main Password + Key + New Main Password + Key

B, Add Temporary Users(Operate in Normal Open)

1, Add Temporary Password (Single Open Mode)

New Temporary Password + Key + New Temporary Password + Key;    Lock Close

2, Add Temporary Card (Single Open Mode)

Read a new card; Lock Close

3, Add Temporary Password and Card (Double Open Mode):

New Temporary Password+ Key + New Temporary Password + Key and Read a Card; Lock Close Or Read a Card and New Temporary Password+ Key + New Temporary Password + Key; Lock Close

C, System Settings:

1, Home Using, Public Mode Switch to Each Other

Main Password + Key + 7 + Key

2, Single Open Mode Switch to Double Open Mode:

Main Password + Key + 6 + Key

3, Double Open Mode Switch to Single Open Mode:

Main Password + Key + 5 + Key

D, Opening

1, Single Open Mode

Password + Key;         Lock Open, Temporary Password and Card Invalid

Read Card;              Lock Open, Temporary Password and Card Invalid

2, Double Open Mode:

Main Password + Key (Or Main Card); Lock Open, Temporary Password and Card Invalid

User Password + Key (Or Card)+ Card (Or Password+key); Lock Open, Temporary Password and Card Invalid

Password ID Card Home Using Lock

1, Factory Reset

Press button on back side of mortise by a thin stick for 5 times, after this step, the lock status will be:

Password: 12345678

Default Mode: Home Using, Single Open

Capacity:

Main Password: 1

User Password: 200

Main Card: 1

User Card: 200

Password: 4~15 digits

2, Change to Home Using Mode

Main Password + Key + 7 + Key : Change to home using mode, lock close

3, Operations:

A, Main Password and Main Card Management

1, Add Main Card:

Lock after factory reset, the first card reading will be the main card;

2, Revise Main Password

Previous Main Password + Key + 1 + New Main Password + Key + New Main Password + Key

B, Add User

1, Add User Password

Main Password + Key + 8 + NO.(001~200) + Key + User Password + Key + User Password + Key

2, Add User Card:

Read Main Card 2 times + Read User Card;

C, Delete User

1, Delete User Password:

Main Password + Key + 4 + No.(001~200) + Key + No.(001~200) + Key;

2, Delete User Card:

Read Main Card 2 Times + 4 + No.(001~200) + Key + No.(001~200)+Key;

3, Delete All User Passwords:

Main Password + Key + 0 + Key

4, Delete All User Cards:

Read Main Card 2 Times + 0 + Key

D, System Settings:

1, Home Using Mode and Public Mode Changing:

Main Password + Key + 7 + Key

2, Single Open Change to Double Open Mode:

Main Password + Key + 6 + Key

3, Double Open Mode Change to Single Open Mode:

Main Password + Key + 5 + Key

E, Open:

1, Single Open:

Read Card;      Lock Open, Close After 5 Seconds

User Password + Key; Lock Open, Close After 5 Seconds

In 5 seconds before lock close, password can be revised:

1 + New Password + Key + New Password + Key;

2, Double Open:

Main Password + Key (or Read Main Card); Lock Open, Close After 5 Seconds

User Password + Key (Or Read User Card) + Read User Card (Or User Password + Key); Lock Open, Close After 5 Seconds

Note: Double Open Mode do not support user password revising.

Note: Input wrong password over 7 times, password panel will be locked for 2 minutes.

D, Other Functions

1, If password invalid, speaker have 3 times “ dee~ “ sound, blue backlight lights down.

2, If low voltage, there is a warning of low voltage, if voltage below the limit, user card can not open lock, only main card can open..

Special Note:

Lock support false password. For example: the right password is 123456, other numbers can add to the start or end of password, like 01234567890 or 78901234560

Features:

Working Voltage: 6.0V (4 AA Batteries)

Power: ＜300mA

Low Voltage Warning: 4.8V

Reading Distance: 0~10cm